## Slide 1: Test Strategies
Testing strategies no matter what area you wish to troubleshoot are based on the same techniques. Remember that when troubleshooting to follow a similar procedure that follows a set structure.

## Slide 2: Test Strategies
Identify the symptoms of the problem – get the facts, ask
Identify the area affected – again get facts, ask
Identify any recently-applied changes
Identify the most likely source of the problem. At this stage you may wish to employ linear or half-split methods to assist in locating the source of the problem
Implement the solution (Remember to Backup System before this stage)
Test the solution
Analyse the possible effects of the solution
(If solution not satisfactory restore backup and implement alternative solution)
Document everything throughout the process

## Slide 3: Example
Scenario: A new housing area is currently being built, and you are working as a member of the construction team.
One day, when the heating technicians are on-site doing checks of the gas boilers in each new house, they report that the last house in the street does not have any gas coming into the house. The piping is installed, of course, but when they turn the gas valve on nothing comes out.

## Slide 4: Example cont/
The gas pipeline servicing these houses is laid out in the following manner:

## Slide 5: Example cont/
Each black dot on the diagram is a shutoff valve, used for isolating different sections of the service pipeline. Based on the heating technician’s report, you conclude that the service pipeline going up to that house must not be “live” and that one of the numbered valves was probably left in the off position. But which one could it be? You know that the main utility connection at the street is “live,” because the gas heater in the contractor mobile building is working just fine. You decide to go to valve number 8 and check for gas pressure at that point in the pipeline with a portable pressure gauge, then checking the pressure at each valve location down the pipeline until you find where there is good gas pressure. However, before you step out of the room to go do this, one of your co-workers suggests you start your search at the middle point of the pipeline instead: at the location of valve. Explain why your co-worker’s idea is better, and also what your next step would be if: (a) you did find pressure at that point, and (b) if you did not find pressure at that point.

## Slide 6: Example Answer
Your co-worker’s strategy is based on the principle of dividing the gas pipeline into halves, and checking for pressure at the half-way point. This troubleshooting strategy is sometimes referred to as the Half-Split or “divide-and-conquer” method, because it divides the system into small sections to optimise troubleshooting time and effort.
This problem gives you a chance to explore the “divide and conquer” strategy of troubleshooting in a context that is very simple and does not require knowledge of computing at all.

## Slide 7: Problem Solving Tools
There are a number of various tools and resources that can help in developing a solution to a problem. These may differ depending on the type of problem.
Can you suggest any tools that maybe used?

## Slide 8: Problem Solving Tools
A flowchart is a diagram that represents a process, they can be simple or quite complex. A flowchart usually incorporates questions and decisions and as such it is a good troubleshooting tool, it ensures that certain options have been investigated and that nothing obvious has been left out.
Lamp Operational

## Slide 9: Problem Solving Tools
Many helpdesks use first-line support in which staff are prompted to ask questions from a script that is shown on a computer screen. The software script, which has been generated from a flowchart, will enable the support technician to lead the user through the problem.
Where the problem is related to a single computer system, using the computers operating System Help facility may help to locate general issues. If a solution is found, attempt to solve the problem and document this in your company faults database, if one exists. See below. If the solution does not work, document that as well, and undo any changes made to the computer.

## Slide 10: Problem Solving Tools
Faults database If you are working in an enterprise, another useful tool often used in problem solving is the Faults Database. This is usually a locally maintained database that contains the problem and resolution of all faults logged within a company. This is a very useful resource, especially as the problems are related to the enterprise infrastructure and systems. If you find a solution, attempt to solve the problem and document the solution. If the solution does not work, document that as well, and undo any changes made to the computer.

## Slide 11: Problem Solving Tools
Searching Internet Resources There are a number of internet resources that can be used to attempt to locate a particular problem. This is accepted practice in industry. You should start with the most reliable sources such as manufacturers online resources and remember that the information you may find on the internet may not always be reliable, so be careful when utilising such information found. Again, document the solution. If the solution does not work, document that as well, and undo any changes made to the computer.
If you do not find a solution, document the information and attempted solutions, and undo any changes made to the computer during the troubleshooting process, you should then escalate the call to someone more experienced, if possible.

## Slide 12: Problem Solving Tools
Debugging tools There are a number of debugging tools that can be employed when problem solving, it is important to know what the tool is used for and how to interpret the results before attempting a solution to rectify the problem. Debugging tools are typically pieces of software that are used to test and debug other programs, hardware or software by enabling step by step execution or logging of information.
Can you suggest any Debugging tools?

## Slide 13: Problem Solving Tools
Desk checking When testing or debugging software, an important troubleshooting tool is to ‘desk check’ a piece of code. This is where you would sit down with a piece of code in front of you and go through it line by line to ensure that you are satisfied it will work. Essentially, running the code in your head before you run the code on your computer.
Other troubleshooting tools include simulators that allow you to simulate a physical system or network and allow you to try solutions that would be too risky or impossible to attempt in a live environment.

## Slide 14: Problem Solving Tools
Investigate Black Box and White Box testing. Write a short report on each of these testing techniques.