## Slide 1
PC won’t power up
Is the power cable securely connected and switched on?
Do the PC LEDs light up?
Does the PC emit a BIOS beep sequence?
Is an image displayed on the monitor?
Does the BIOS POST test run?
Does the BIOS memory test run?
Do Windows begin to load?
The processor fan should start spinning when the LEDs come on.
The BIOS should issue one or more beeps when your PC powers up.
Check that all internal hardware cards are secure in their slots
Troubleshoot your hard drive problems (Use Tools to fix HD).
Check power cable is secure. Use a replacement if needed.
Open the case and check all internal cables are secure. Does the PC boot?
Is the internal speaker connected?
Are monitor cables securely connected? Try a different monitor.
Identify the problem via the beep code sequence.
Replace faulty RAM.
Resolve your Windows start-up problems. (Use Windows Tools)
Replace the power supply.
Motherboard faulty: replace.
Graphics card faulty: replace.
Troubleshoot the beep code error.
(Use BIOS Beep Code Ref.)
Yes
Yes
Yes
Yes
Yes
Yes
Yes
No
No
No
No
No
No
Yes
No
Yes
Yes
No